FOR IMMEDIATE RELEASE

## October 23, 2018

Headline:  That’s a Wrap for Robbins Rock Machine ‘Driller Mike’

Sub-Headline: Tough TBM and Team overcome the odds with Atlanta breakthrough

On October 4, 2018, onlookers watched as a 3.8 m (12.5 ft) diameter Robbins Main Beam TBM completed its epic journey. The TBM, christened “Driller Mike”, after local rapper and activist “Killer Mike”, overcame extremely hard rock conditions along a curving 8.0 km (5.0 mi) tunnel to bolster the city of Atlanta, Georgia, USA’s water supply.

The new tunnel brings the Atlanta Water Supply Program one step closer to increasing the city’s water capacity to between 30 and 90 days depending on daily usage. “Our schedule for the project was very aggressive but the project team stayed together to overcome issues related to the mining of the tunnel,” said Bob Huie, Project Director for the PC Russell JV, the Construction Manager at Risk (CMAR) for the project.

The unique structure of the project team is credited with the overall project success despite challenges. “I’m proud of our team. They had obstacles and challenges and challenging ground, but they stuck together and didn’t give up, and they were successful. There was great leadership and supervision all around,” said Larry Weslowski, Tunnel Superintendent for the PC Russell JV.

The project is only the third such large construction project in the U.S. to use the CMAR structure.  The PC Construction/HJ Russell JV was selected as the CMAR for the project, who then purchased the Robbins Main Beam TBM for the tunnel.  The designer for the construction works including tunnel and shafts, JP2—consisting of Stantec, PRAD Group, Inc., and River 2 Tap—specified the hard rock TBM.  Operation and assembly of the TBM was then sub-contracted to the Atkinson/Technique JV.

The robust TBM was assembled using Onsite First Time Assembly (OFTA) at the massive Bellwood Quarry site with help from Robbins personnel. “The guys built everything per the specs to help with scheduling. It was a challenge but there was no negativity during the process,” said Weslowski. Despite summer temperatures hitting 43 degrees Celsius (110 degrees Fahrenheit) and 100 percent humidity, the TBM was ready to launch by October 2016.

Hard granitic rock challenged the 19-inch disc cutters from the outset. “There was ground so hard that it would take eight hours to go 1.5 m (5 ft). It was between 117 and 310 MPa (17,000 and 45,000 psi) UCS. The beginning of the job was tough,” said Weslowski, but he added that once the learning curve had been overcome “they started breaking project records left and right towards the end.  We got a best day of 38.4 m (126 ft). Rates just kept increasing.”

Other challenges included groundwater encountered during tunneling. “We did encounter groundwater contamination that required remediation. This remediation work was completed successfully,” said Huie.

With tunneling complete, the USD $300 million project for the City of Atlanta’s Department of Watershed Management is on track to meet its scheduled overall completion date of September 2019. The project will turn the inactive Bellwood quarry into a 9.1 billion liter (2.4 billion gallon) raw water storage facility connecting with the Chattahoochee River and various water treatment facilities.

WORD COUNT: 505

Side bar or callout text:

The News in Brief:

--A 3.8 m (12.5 ft) diameter Robbins Main Beam TBM broke through at the Atlanta Water Supply Program in Georgia, USA on October 4, 2018.

-- The TBM, christened “Driller Mike”, after local rapper and activist “Killer Mike”, overcame extremely hard rock conditions on an 8.0 km (5.0 mi) tunnel.
--The Robbins TBM and 19-inch disc cutters were challenged by extremely hard granitic rock between 117 and 310 MPa (17,000 and 45,000 psi) UCS.
--Despite the challenges, the Robbins TBM achieved a best day of 38.4 m (126 ft).
--The Atlanta Water Supply Program will turn the inactive Bellwood quarry into a 9.1 billion liter (2.4 billion gallon) raw water storage facility connecting with the Chattahoochee River and various water treatment facilities.

Images Attached to Email.  If you need a higher resolution image, please contact Desiree Willis.

Captions for Images:

Image 1: The PC Russell JV and Atkinson/Technique JV celebrate the breakthrough of the Robbins TBM on October 4, 2018 in Atlanta, Georgia, USA.

Image 2:  The Robbins TBM and 19-inch cutters overcame exceedingly hard granitic rock at strengths up to 310 MPa (45,000 psi) UCS.

Image 3: Crews are proud of the coordination required to overcome a host of challenges, including tight tunnel curves and contaminated groundwater that required remediation.

Image 4: The robust TBM was assembled using Onsite First Time Assembly (OFTA) at the massive Bellwood Quarry site with help from Robbins personnel.

## Desiree Willis

#### Technical Writer

Email: willisd@robbinstbm.com

Direct: 253.872.4490

##### The Robbins Company

29100 Hall Street

Solon, OH 44139

USA